## Slide 1: Microwave communication

## Slide 2
Name : Mubashir Ali
Roll No: 2k20/ITE/73
Topic: Microwave Communication

## Slide 3: What is Microwave Communication
A communication system that utilizes the radio frequency band spanning 2 to 60 GHz. As per IEEE, electromagnetic waves between 30 and 300 GHz are called millimeter waves (MMW) instead of microwaves as their wavelengths are about 1 to 10mm.

## Slide 4: What is Microwave Communication
Small capacity systems generally employ the frequencies less than 3 GHz while medium and large capacity systems utilize frequencies ranging from 3 to 15 GHz. Frequencies > 15 GHz are essentially used for short-haul transmission.

## Slide 5: Advantages of Microwave Radio
•
•
•
Less affected by natural calamities Less prone to accidental damage
Links across mountains and rivers are more economically feasible
Single point installation and maintenance Single point security
They are quickly deployed
•
•
•

## Slide 6: Line-of-Sight Considerations
•
Microwave radio communication requires a clear line-of- sight (LOS) condition
Under normal atmospheric conditions, the radio horizon is around 30 percent beyond the optical horizon
Radio LOS takes into account the concept of Fresnel ellipsoids and their clearance criteria
•
•

## Slide 7: Line-of-Sight Considerations
•
Fresnel Zone - Areas of constructive and destructive interference created when electromagnetic wave propagation in free space is reflected (multipath) or diffracted as the wave intersects obstacles. Fresnel zones are specified employing ordinal numbers that correspond to the number of half wavelength multiples that represent the difference in radio wave propagation path from the direct path
•
The Fresnel Zone must be clear of all obstructions.

## Slide 8: Microwave Link Design
Microwave Link Design is a methodical, systematic and sometimes lengthy process that includes
•
•
•
•
Loss/attenuation Calculations
Fading and fade margins calculations
Frequency planning and interference calculations Quality and availability calculations

## Slide 9: Microwave Link Design Process
The whole process is iterative and may go through many redesign phases before the required quality and availability are achieved
Multipath propagation
Frequency Planning
Link Budget
Quality and
Availability Calculations
Fading Predictions
Interference analysis
Propagation losses
Branching losses
Other Losses
Rain attenuation
Diffraction- refraction losses

## Slide 10: Loss / Attenuation Calculations
The loss/attenuation calculations are composed of three main contributions
Propagation losses
(Due to Earth’s atmosphere and terrain)
Branching losses
(comes from the hardware used to deliver the transmitter/receiver output to/from the antenna)

## Slide 11: Loss / Attenuation Calculations
– Miscellaneous (other) losses
(unpredictable and sporadic in character like fog, moving objects crossing the path, poor equipment installation and less than perfect antenna alignment etc)
This contribution is not calculated but is considered in the planning process as an additional loss

## Slide 12: Propagation Losses
•
Obstacle Loss –also called Diffraction Loss or Diffraction Attenuation. One method of calculation is based on knife edge approximation.
Having an obstacle free 60% of the Fresnel zone gives 0 dB loss
0 dB
20dB
16dB
6dB
0 dB
First Fresnel Zone

## Slide 13: Propagation Losses
•
Gas absorption
– Primarily due to the water vapor and oxygen in the atmosphere in the radio relay region.The absorption peaks are located around 23GHz for water molecules and 50 to 70 GHz for oxygen molecules.The specific attenuation (dB/Km)is strongly dependent on frequency, temperature and the absolute or relative humidity of the atmosphere.

## Slide 14: Gas attenuation versus frequency
Total specific gas attenuation 23GHz |  | 
(dB/Km) | T=40oC RH=80% T=30o RH=50 Frequency (GHz | 
%
)
0
25
50
0.4
1.0

## Slide 15: Propagation Losses
•
Attenuation due to precipitation
Rain attenuation is the main contributor in the frequency range used by commercial radio links
Rain attenuation increases exponentially with rain intensity
The percentage of time for which a given rain intensity is attained or exceeded is available for 15 different rain zones covering the entire earth’s surface

## Slide 16: Propagation Losses
The specific attenuation of rain is dependent on many parameters such as the form and size of distribution of the raindrops, polarization, rain intensity and frequency
Horizontal polarization gives more rain attenuation than vertical polarization
Rain attenuation increases with frequency and becomes a major contributor in the frequency bands above 10 GHz
The contribution due to rain attenuation is not included in the link budget and is used only in the calculation of rain fading

## Slide 17: Ground Reflection
•
Reflection on the Earth’s surface may give rise to multipath propagation
The direct ray at the receiver may interfered with by the ground-reflected ray and the reflection loss can be significant
Since the refraction properties of the atmosphere are constantly changing the reflection loss varies.
•
•

## Slide 18: Ground Reflection
•
The loss due to reflection on the ground is dependent on the total reflection coefficient of the ground and the phase shift
The highest value of signal strength is obtained for a phase angle of 0o and the lowest value is for a phase angle of 180o
The reflection coefficient is dependent on the frequency, grazing angle (angle between the ray beam and the horizontal plane), polarization and ground properties
•
•

## Slide 19: Ground Reflection
•
The grazing angle of radio-relay paths is very small – usually less than 1o
It is recommended to avoid ground reflection by shielding the path against the indirect ray
The contribution resulting from reflection loss is not automatically included in the link budget.When reflection cannot be avoided, the fade margin may be adjusted by including this contribution as “additional loss” in the link budget
•
•

## Slide 20: Link Budget
The link budget is a calculation involving the gain and loss factors associated with the antennas, transmitters, transmission lines and propagation environment, to determine the maximum distance at which a transmitter and receiver can successfully operate

## Slide 21: Link Budget
•
Receiver sensitivity threshold is the signal level at which the radio runs continuous errors at a specified bit rate
•
System gain depends on the modulation used (2PSK, 4PSK, 8PSK, 16QAM, 32QAM, 64QAM,128QAM,256QAM) and on the
design of the radio

## Slide 22: Link Budget
•
The gains from the antenna at each end are added to the system gain (larger antennas provide a higher gain).
The free space loss of the radio signal is subtracted. The longer the link the higher the loss
These calculations give the fade margin
In most cases since the same duplex radio setup is applied to both stations the calculation of the received signal level is independent of direction
•
•
•

## Slide 23: Link Budget
•
The fade margin is calculated with respect to the receiver threshold level for a given bit-error rate (BER).The radio can handle anything that affects the radio signal within the fade margin but if it is exceeded, then the link could go down and therefore become unavailable

## Slide 24: Link Budget
•
The threshold level for BER=10-6 for microwave equipment used to be about 3dB higher than for BER=10-3.
Consequently the fade margin was 3 dB larger for BER=10-6 than BER=10-3. In new generation microwave radios with power forward error correction schemes this difference is
0.5 to 1.5 dB

## Slide 25: Radio path link budget
24
Transmitter 1
Receiver 1
Splitter
Splitter
Transmitter 2
Receiver 2
Output Power (Tx)
Branching Losses
waveguide
Propagation
Losses
Antenna Gain
Antenna Gain
Branching Losses
Received Power (Rx)
Receiver threshold Value
Fade Margin

## Slide 26: Fading and Fade margins
Fading is defined as the variation of the strength of a received radio carrier signal due to atmospheric changes and/or ground and water reflections in the propagation path.Four fading types are considered while planning links.They are all dependent on path length and are estimated as the probability of exceeding a given (calculated) fade margin

## Slide 27: Fading and Fade margins
•
Multipath fading
Flat fading
Frequency-selective fading
•
•
Rain fading
Refraction-diffraction fading (k-type fading)

## Slide 28: Fading and Fade margins
•
Multipath Fading is the dominant fading mechanism for frequencies lower than 10GHz. A reflected wave causes a multipath, i.e.when a reflected wave reaches the receiver as the direct wave that travels in a straight line from the transmitter
If the two signals reach in phase then the signal amplifies. This is called upfade
•

## Slide 29: Fading and Fade margins
•
Upfademax=10 log d – 0.03d (dB) d is path length in Km
If the two waves reach the receiver out of phase they weaken the overall signal.A location where a signal is canceled out by multipath is called null or downfade
As a thumb rule, multipath fading, for radio links having bandwidths less than 40MHz and path lengths less than 30Km is described as flat instead of frequency selective
•
•

## Slide 30: Fading and Fade margins
Flat fading
•
•
A fade where all frequencies in the channel are equally affected.There is barely noticeable variation of the amplitude of the signal across the channel bandwidth
If necessary flat fade margin of a link can be improved by using larger antennas, a higher-power microwave transmitter, lower –loss feed line and splitting a longer path into two shorter hops
On water paths at frequencies above 3 GHz, it is advantageous to choose vertical polarization

## Slide 31: Fading and Fade margins
Frequency-selective fading
•
•
•
There are amplitude and group delay distortions across the channel bandwidth
It affects medium and high capacity radio links (>32 Mbps)
The sensitivity of digital radio equipment to frequency- selective fading can be described by the signature curve of the equipment
This curve can be used to calculate the Dispersive Fade Margin (DFM)

## Slide 32: Fading and Fade margins
•
Rain Fading
Rain attenuates the signal caused by the scattering and absorption of electromagnetic waves by rain drops
It is significant for long paths (>10Km)
It starts increasing at about 10GHz and for frequencies above 15 GHz, rain fading is the dominant fading mechanism
Rain outage increases dramatically with frequency and than with path length

## Slide 33: Thank you